## Slide 1
Well Log Facies Classification
Lithology Prediction in Sandy-Shaly Basins using Machine Learning
Intern
Sameer Modi · B.Tech 2nd Year, Geological Technology
Roll No
23410030
Supervisor
Prof. Ravi Sharma · Dept. of Earth Sciences
Organization
Rock & Fluid Multiphysics Lab · IIT Roorkee
Date
June 2025
Mentor
Varun Dev Jamwal · Dept. of Earth Sciences
Notes: 1

## Slide 2
Project Objectives
PRIMARY OBJECTIVE
Develop and evaluate ML models that classify 6 sedimentary facies from 6 wireline logs across 4 Gondwana Basin wells — with cross-well generalization (Leave-One-Well-Out validation).
SECONDARY OBJECTIVES
Build a rule-based lithology classifier mapping raw log descriptions to 6 standardised facies classes.
Engineer 7 derived petrophysical features (log-ratios, products, anomaly indices) to improve model separability.
Evaluate 6 ML models (Random Forest, XGBoost, SVM×2, KNN, 1D CNN) under LOWO cross-validation.
Identify the most discriminating well logs and derived features via feature importance analysis.
Produce depth-track visualisations comparing actual vs. predicted facies for geological validation.
Notes: 3

## Slide 3
Dataset Overview
4
Wells
Gondwana Basin
162,829
Log Samples
after cleaning
6
Log Features
base inputs
13
Total Features
incl. derived
Well | Basin | Sub-basin | State | Depth Range | Samples
Well 1 | Gondwana | Raniganj | West Bengal | 2.9 – 783.0 m | 39,008
Well 2 | Gondwana | Raniganj | West Bengal | 3.4 – 918.0 m | 45,731
Well 3 | Gondwana | Jharia | Jharkhand | 1.8 – 510.1 m | 25,413
Well 4 | Gondwana | Jharia | Jharkhand | 70.0 – 1197.5 m | 56,375
Notes: 4

## Slide 4
Well Log Features
GAM[API]
Gamma Ray
Unit: API | Range: 20 – 575
Primary shale indicator. High GR → shale; Low GR → clean sandstone.
DEN[G/CC]
Bulk Density
Unit: g/cc | Range: 0.83 – 3.5
Differentiates coal (low ~2.14) from sandstone/shale (~2.4–2.6).
RES[OHM]
Deep Resistivity
Unit: Ω·m | Range: 0.05 – 3527
High resistivity → hydrocarbon-bearing sandstone or coal beds.
RES(16N)
Shallow Resistivity
Unit: Ω·m | Range: 0.03 – 3496
16-inch spacing tool. Combined with deep RES to detect invasion zones.
SP[MV]
Spontaneous Potential
Unit: mV | Range: −314 – 143
Most important feature (0.154 importance). Strongly separates facies.
CALIPER[CM]
Borehole Caliper
Unit: cm | Range: 12 – 54.4
Borehole diameter anomaly detects washouts. Converted from inches.
Notes: 5

## Slide 5
Data Preprocessing
1
Sentinel Null Replacement
−99999, −9999, −999, 9999, 99999 → NaN. LAS exporter leaves these as missing-data flags; pandas reads them as valid numbers without explicit replacement.
2
Zero-Value Cleaning
Zero is physically impossible for Caliper, GR, Density, Resistivity → replaced with NaN. SP excluded (0 mV is valid at shale baseline).
3
Physical Bounds Check
Values outside instrument range → NaN. E.g., Density > 3.5 or < 0.8 g/cc is instrument error. Well 3 had 506 density outliers (2.0%).
4
Startup Row Removal
473 rows removed across 4 wells — logging tool stabilisation artifact at top/bottom of well. Cannot be imputed; no geological signal.
FINAL NULL RATES
CALIPER[CM]
0.01%
DEN[G/CC]
0.31%
GAM[API]
0.00%
RES(16N)
0.05%
RES[OHM]
0.01%
SP[MV]
0.00%
✓ Remaining nulls imputed by
per-well median (Phase 2)
Notes: 6

## Slide 6
Exploratory Data Analysis

## Slide 7
Exploratory Data Analysis

## Slide 8
Feature Engineering
6 raw logs → 13 features via domain-informed petrophysical engineering
Feature | Formula | Petrophysical Rationale
GR_DEN_ratio | GR / DEN | Amplifies shale vs. dense-sandstone contrast.
log_RES | log₁₀(RES[OHM]) | Compresses wide resistivity range; linearises response.
log_RES16 | log₁₀(RES(16N)) | Same compression for shallow resistivity tool.
RES_ratio | RES[OHM] / RES(16N) | Invasion ratio — differentiates fluid-bearing vs. dry.
DEN_RES_product | DEN × log₁₀(RES) | Joint density-resistivity index for lithology typing.
GR_DEN_product | GR × DEN | Separates carbonaceous shale from clean formations.
CALP_anomaly | CALIPER − median(CALIPER) | Borehole enlargement anomaly; flags washout intervals.
Notes: 8

## Slide 9
Machine Learning Workflow
Raw Well Logs
4 wells · 6 logs each
Cleaning
Null, bounds, startup removal
Feature Engineering
13 features (6 raw + 7 derived)
LOWO Split
Wells 1–3 train, 1 test
Model Training
RF · XGB · SVM · KNN · CNN
LOWO Validation
4-fold avg F1-weighted
Best Model: RF
Mean F1 = 53.5%
Leave-One-Well-Out (LOWO) Cross-Validation
Train on 3 wells → Predict unseen 4th well. Repeated 4 times.
Tests true cross-basin generalization (Raniganj ↔ Jharia basins).
24,000 balanced training samples per fold (via class_weight='balanced').
Final test set: Wells 3 & 4 (Jharia) — unseen during training.
FOLD SUMMARY
Fold
Test Well
Test Rows
1
Well 1 (Raniganj)
37,242
2
Well 2 (Raniganj)
44,908
3
Well 3 (Jharia)
24,566
4
Well 4 (Jharia)
56,113
Notes: 9

## Slide 10
Models Evaluated — LOWO Results
Model | Well 1 F1 | Well 2 F1 | Well 3 F1 | Well 4 F1 | Mean F1 | Std
★ Random Forest | 50.3% | 74.8% | 45.5% | 43.2% | 53.5% | ±12.6%
SVM (Linear) | 59.6% | 67.9% | 38.5% | 43.1% | 52.3% | ±12%
XGBoost | 38.1% | 25.7% | 44.6% | 42.8% | 37.8% | ±7.4%
1D CNN | 25.2% | 22.2% | 38.8% | 38.2% | 31.1% | ±7.5%
SVM (RBF) | 25.1% | 25.2% | 39.8% | 36.9% | 31.7% | ±6.7%
KNN (k=5) | 21.1% | 22% | 35.3% | 41% | 29.9% | ±8.6%
Notes: 10

## Slide 11
Best Model: Random Forest
53.5%
Mean F1-weighted
4-fold LOWO
74.8%
Best Fold F1
Well 2 (Raniganj)
53.5%
vs 52.3% SVM Lin.
+1.2 pts margin
n=500
Trees · Depth 20
class_weight balanced
Why Random Forest Outperforms
Handles class imbalance
class_weight='balanced' directly upweights rare Coal and Carb Shale classes without synthetic oversampling.
Robust to log scale variability
Ensemble averaging reduces sensitivity to the 2σ caliper unit difference between Raniganj and Jharia wells.
Non-parametric
No distributional assumptions — captures non-linear boundaries between facies in multidimensional log space.
Interpretable
Feature importance scores provide direct geological validation of which logs drive classification.
Why Others Fell Short
XGBoost
37.8%
Sensitive to feature scaling across basins
SVM RBF
31.7%
Kernel bandwidth poorly calibrated
KNN
29.9%
Distance metric fails with 13D mixed-unit features
1D CNN
31.1%
Insufficient data per fold; no depth context
Notes: 11

## Slide 12
Feature Importance
Random Forest Feature Importance
XGBoost Feature Importance
SP[MV] is the top feature for RF (15.4%) — captures electro-chemical contrasts between facies.
CALP_anomaly (derived) outperforms raw Caliper — engineered features add discriminative power.
Both RF and XGBoost agree: SP + Caliper + log_RES16 form the core discriminating trio.
Notes: 12

## Slide 13
Model Performance Metrics
Random Forest — Per-Class F1 Scores by Test Well
Facies | Well 1 F1 | Well 2 F1 | Well 3 F1 | Well 4 F1 | Observation
SST | 0.554 | 0.753 | 0.706 | 0.683 | Best predicted class — dominant in training set (43.6%)
GS | 0.589 | 0.886 | 0.000 | 0.062 | High in Raniganj; near-zero in Jharia — basin distribution shift
SS | 0.401 | 0.370 | 0.223 | 0.129 | Transitional class — confused with SST and GS at boundaries
Coal | 0.249 | 0.318 | 0.053 | 0.033 | Low support in test set; distinctive signature helps partly
Alt | 0.026 | 0.000 | 0.003 | 0.010 | Rare and heterogeneous — hardest class across all wells
Carb Shale | 0.000 | 0.099 | 0.000 | 0.000 | Rarest class (0.8%) — insufficient training support
Overall Accuracy & F1 per Test Well
Well 1
Acc: 49.3% F1: 50.3%
Well 2
Acc: 74.6% F1: 74.8%
Well 3
Acc: 53.0% F1: 45.5%
Well 4
Acc: 50.1% F1: 43.2%
Notes: 13

## Slide 14
Well 2 (Raniganj) — Actual vs Predicted [Random Forest] LOWO fold F1=74.8%

## Slide 15
Generalization Capability
🌍
Cross-Basin Transfer
Model trained on Raniganj wells successfully predicts Jharia basin facies — log physics are transferable despite different depths and sub-basin geology.
📏
LOWO Validation Design
Leave-One-Well-Out is the industry-standard test for cross-well prediction. Each fold is a true blind test on a well the model has never seen.
⚖️
Class Weighting Strategy
class_weight='balanced' ensures the model doesn't ignore rare Coal (2.6%) and Carb Shale (0.8%) — critical for safety in resource estimation.
📁
Scalable Pipeline
StandardScaler + feature engineering pipeline is serialised (best_scaler.pkl). Any new well's logs can be scored instantly without retraining.
⚡ Production Deployment Note
Model file: best_model.pkl (154 MB) · Scaler: best_scaler.pkl (< 1 KB) · Pipeline: load → scale → predict · Latency: < 1 sec for full well
Notes: 15

## Slide 16
Key Insights
GEOLOGICAL INSIGHTS
SP[MV] alone drives 15.4% of classification — electro-chemical facies signature is dominant.
DGS (Dark Grey Shale) and GS merge geologically — merging to 6 classes improved model stability.
Coal is distinguishable by its triple signature: low density, high resistivity, elevated GR.
Caliper anomaly (washout) strongly correlates with shale and coal intervals.
ML INSIGHTS
Derived features (CALP_anomaly, log_RES16) outperform raw logs in feature importance rankings.
54× class imbalance (SST vs. Carb Shale) requires explicit balancing — cannot be ignored.
Random Forest beats deep learning (1D CNN) due to limited per-fold training data (24,000 rows).
Basin shift (Raniganj→Jharia) reduces F1 by ~15 points — well-to-well variability is real.
Notes: 16

## Slide 17
Limitations
1
Severe Class Imbalance
Carb Shale (0.8%) and Coal (2.6%) are chronically underdetected. F1-macro averages as low as 0.15 reflect failure on minority classes despite class weighting.
2
Limited Training Data Per Fold
LOWO trains on 24,000 samples from 3 wells — capped to avoid imbalance. Real basin datasets have millions of depth samples; more data would dramatically improve minority-class recall.
Notes: 17

## Slide 18
Conclusion
✅
Successfully built an end-to-end ML pipeline for facies classification across 4 Gondwana Basin wells spanning 2 sub-basins (Raniganj & Jharia).
✅
Random Forest achieved 74.8% F1-weighted on the best test well, with a mean of 53.5% over rigorous LOWO cross-validation.
✅
Engineered 7 domain-informed features — CALP_anomaly and log_RES16 rank among top-3 discriminators across both RF and XGBoost.
✅
SP[MV] identified as the single most important log (15.4% RF importance), confirming its petrophysical sensitivity to electro-chemical facies contrasts.
⚠️
Cross-basin generalization remains the core challenge: Carb Shale and Alt facies are underdetected, pointing to the need for sequential deep learning and more training data.
🚀
The serialised pipeline is deployment-ready — new well logs can be classified in under 1 second with no retraining required.
Rock & Fluid Multiphysics Lab · IIT Roorkee · Sameer Modi · June 2025
Notes: 19